## Slide 1
PCB artwork:
Make a business card
Alex Tait
atait@ieee.org

## Slide 2: Objectives
Download KiCAD and Inkscape
Find/create/remix some vector artwork
Single layer import (KiCAD)
Multi-layer designs (inkscape)
Convert to footprints (svg2mod)
Insert a footprint into a pcbnew file
Submit PCB designs to fabrication house
Fabricate PCBs
Pick up from Resistor
Skip over kicad_pro and eeschema

## Slide 3: Workshop outline
Hour 1: Importing graphics
  20 min talking
    Printed circuit boards
    Computer aided design (CAD)
    Layout primitives (lines, curves)
  30 min asynchronous
    Download KiCAD
    Obtain template files
    Edit text
    Import basic Resistor logo (from SVG file)
    Notice the primitive shapes
  10 min break
Hour 2: Editing graphics
  30 min talking
    Computer graphics
    SVG/PCB Layers
    Path operations
  20 min asynchronous
    Download Inkscape
    Find and download a vector image
    Import, version, and begin editing
    Notice colors and layers
  10 min break
Hour 3: Custom footprints
  10 min talking
    KiCAD footprints
    KiCAD local libraries
    PCB fabrication + economics
  50 min asynchronous
    Place fancy Resistor logo (from footprint Library)
    Use svg2mod to generate your own footprint
    Upload to JLCPCB and play with pricing options
    Continue editing your footprint until finished
Afterwards
- continue working at your own pace
- follow instructions to upload to OSHPARK
- email/discord for tech support

## Slide 4: Provided assets
Business card template (bcard_template.pcbnew)
  With LocalLib on the paths
Resistor logo (resistor_logo.svg)
Resistor logo footprint (resistor_logo2.kicad_mod)
  Inside LocalLib/modules

## Slide 5: Obtaining the repo
Git clone...

## Slide 6: How asynchronous sessions will work
Learn the procedure by reproducing the NYCRESISTOR example design
Then repeat the procedure on your own design
Each session, we start from checkpoint X, try to get to checkpoint X+1
All the example checkpoint files are in the repo
If you reproduce the example early, move to your own design or help others
If not, no problem, you’ll be able to catch up at the next checkpoint
The last hour is all asynchronous work time

## Slide 7: Asynchronous 1
Clone the repo
Download Inkscape
Download KiCAD
Meet your neighbors. You will be helping each other later
  Name
  Pronouns
  Relationship to NYC Resistor
  Something you are working on or want to work on

## Slide 9: Computer Graphics

## Slide 10: Computer Graphics: Vector vs. Raster
And anchor points
a.k.a., a picture
.png (portable network graphics)
.jpeg
.bmp
.svg (scalable vector graphics)

## Slide 11: Computer Graphics: Vector vs. Raster
Most things can be visualized as vector or raster
So which way is better?
Credit: Clemson Intro to GIS

## Slide 12: Graphics for PCB hardware
Electrical wires are lines
Always vectorized eventually

## Slide 13: Converting: vector ↔ raster
Which is easier?

## Slide 14: KiCAD-native graphics imports
SVG
  Single layer
Bitmap
  Single color
Asynchronous interactive time

## Slide 15: What is a PCB

## Slide 16: Stackup

## Slide 17: Solder mask colors
Usually green
Also: blue, black
Less common: red, white, yellow, purple, etc.

## Slide 18: Copper finish colors
Silver or gold
That’s pretty much all we care about today

## Slide 19: Layout design

## Slide 20: Old fashioned style

## Slide 21: KiCAD
Modern circuit + layout design

## Slide 22: Vector import dialog

## Slide 23: Editing vector graphics

## Slide 24: Inkscape
Tips

## Slide 25: Vocab
Point / node
Segment
  Line, or Curve
Path
  Polygon

## Slide 26: Boolean operations
Boolean is a term from logic, something True or False...
  In digital electronics: True = 5 Volts, False = 0 Volts
Operation: two things in, one thing out
  A + B = C
  A x B = D
In vector graphics: inputs and outputs are shapes
  True = inside, False = outside
+
A
B
C
+
x

## Slide 27: Boolean operations
Shape A
Shape B
Point 1
Point 2
Intersection (a.k.a. AND):
”Point 2 is inside shape A and inside shape B, so Point 2 is inside the output shape”
Union (a.k.a. OR):
”Point 2 is inside shape A or inside shape B, so Point 2 is inside the output shape”
Repeat this logic for every point

## Slide 28: Inset/outset operations
This is very useful for us

## Slide 29: Scale operations
Make things the right size
Locking the aspect ratio

## Slide 30: Layers in SVG
Naming
Hiding/Showing
Ordering
Coloring

## Slide 31: SVG Layers for PCB design
F.x (front) B.x (back)
x.Cu = copper
So F.Cu = front copper
x.Mask layers are inverted
  Shapes on Mask layers will be openings in the solder mask

## Slide 32: Multi-layer graphics

## Slide 33: Workflow
Open Terminal
Install `svg2mod`
Move shapes to named layers
Use svg2mod to convert
Open footprint editor
Import the new footprint
Insert into board
Inspect in 3D

## Slide 34: Conversion step
Edit SVG paths

## Slide 35: Uploading a PCB for fabrication

## Slide 36: Workflow
Starting in .kicad_pcb
Review 3D + ERC (good practice)
Plot gerbers
Zip folder of gerbers
Drag-drop to JLCPCB
Inspect upload

## Slide 37: Plotting gerbers
Print
Do not use this
Plot

## Slide 38: Plotting gerbers
Don’t leave this field blank
Check that these are selected
Deselect X2 format
Deselect these
First click Drill Files and press OK in the new popup
Finally, press PLOT here

## Slide 39: Compressing to zip archive
Right click
Windows/Linux: google how to zip a directory

## Slide 40: Uploading to JLCPCB
drag,drop

## Slide 41: Inspect upload

## Slide 42: Configuring the physical properties

## Slide 43: Properties you can change
Quantity
Core Material
PCB Thickness
Soldermask Color
Surface Finish
We will not need the rest of the properties

## Slide 44: Offloads

## Slide 45: Our group order costs
Defaults: funded by the workshop ticket price
  5x qty
  Any color
  1.6mm thickness
  Silver surface finish
  Fiberglass core
Add-ons: cost extra
  Greater qty
  Gold surface finish
  Other thicknesses
  Aluminum or copper core
We’re making add-ons available individually and at-cost
Calculated Price
Subtract $2.00
Shipping Estimate
Subtract $29.16
Upload zip file
Select options
Venmo Resistor this amount
Add
Resistor pays JLCPCB

## Slide 46: Pricing add-ons: example 1
Suppose I want
  30x qty
  Black mask
  Gold finish
Boards: $51.20 – $2.00 = $49.20
Excess shipping: $30.77 – $29.16 = $1.61
I would Venmo Resistor $49.20 + $1.61 = $50.81 on top of the ticket price
Note: the numbers you get will differ based on size of board

## Slide 47: Pricing add-ons: example 2
Suppose I want
  100x qty
  Lead-free silver finish
Boards: $50.40 – $2.00 = $48.40
Excess shipping: $93.47 – $29.16 = $64.31
I would Venmo Resistor $48.40 + $64.31 = $112.71
Because 100x is significantly heavier than 5x
Note: the numbers you get will differ based on size of board

## Slide 48: Raster import program (bitmap2component)

## Slide 49: Raster import program